## Slide 1: ELEG 3124 SYSTEMS AND SIGNALS Ch. 1 Continuous-Time Signals
Dr. Jingxian Wu
wuj@uark.edu

## Slide 2: OUTLINE
Introduction: what are signals and systems?
Signals
Classifications
Basic Signal Operations
Elementary Signals

## Slide 3: INTRODUCTION
Examples of signals and systems (Electrical Systems)
  Voltage divider
    Input signal: x = 5V
    Output signal: y = Vout
    The system output is a fraction of the input (
  Multimeter
    Input: the voltage across the battery
    Output: the voltage reading on the LCD display
    The system measures the voltage across two points
  Radio or cell phone
    Input: electromagnetic signals
    Output: audio signals
    The system receives electromagnetic signals and convert them to audio signal
Voltage divider
multimeter

## Slide 4: INTRODUCTION
Examples of signals and systems (Biomedical Systems)
  Central nervous system (CNS)
    Input signal: a nerve at the finger tip senses the high
    temperature, and sends a neural signal to the CNS
    Output signal: the CNS generates several output signals
    to various muscles in the hand
    The system processes input neural signals, and generate
    output neural signals based on the input
  Retina
    Input signal: light
    Output signal: neural signals
    Photosensitive cells called rods and cones in the retina convert incident light energy into signals that are carried to the brain by the optic nerve.
Retina

## Slide 5: INTRODUCTION
Examples of signals and systems (Biomedical Instrument)
  EEG (Electroencephalography) Sensors
    Input: brain signals
    Output: electrical signals
    Converts brain signal into electrical signals
  Magnetic Resonance Imaging (MRI)
    Input: when apply an oscillating magnetic field at a certain frequency, the hydrogen atoms in the body will emit radio frequency signal, which will be captured by the MRI machine
    Output: images of a certain part of the body
    Use strong magnetic fields and radio waves to form images of the body.
MRI
EEG signal collection

## Slide 6: INTRODUCTION
Signals and Systems
  Even though the various signals and systems could be quite different, they share some common properties.
  In this course, we will study:
    How to represent signal and system?
    What are the properties of signals?
    What are the properties of systems?
    How to process signals with system?
  The theories can be applied to any general signals and systems, be it electrical, biomedical, mechanical, or economical, etc.

## Slide 7: OUTLINE
Introduction: what are signals and systems?
Signals
Classifications
Basic Signal Operations
Elementary Signals

## Slide 8: SIGNALS AND CLASSIFICATIONS
What is signal?
  Physical quantities that carry information and changes with respect to time.
  E.g. voice, television picture, telegraph.
Electrical signal
  Carry information with electrical parameters (e.g. voltage, current)
  All signals can be converted to electrical signals
    Speech  Microphone  Electrical Signal  Speaker  Speech
  Signals changes with respect to time
8
audio signal

## Slide 9: SIGNALS AND CLASSIFICATIONS
Mathematical representation of signal:
  Signals can be represented as a function of time t
  Support of signal:
  E.g.
  E.g.
    and are two different signals!
  The mathematical representation of signal contains two components:
    The expression:
    The support:
      The support can be skipped if
      E.g.
9

## Slide 10: SIGNALS AND CLASSIFICATIONS
Classification of signals: signals can be classified as
  Continuous-time signal v.s. discrete-time signal
  Analog signal v.s. digital signal
  Finite support v.s. infinite support
  Even signal v.s. odd signal
  Periodic signal v.s. Aperiodic signal
  Power signal v.s. Energy signal
  ……
10

## Slide 11: OUTLINE
Introduction: what are signals and systems?
Signals
Classifications
Basic Signal Operations
Elementary Signals

## Slide 12: SIGNALS: CONTINUOUS-TIME V.S. DISCRETE-TIME
Continuous-time signal
  If the signal is defined over continuous-time, then the signal is a continuous-time signal
    E.g. sinusoidal signal
    E.g. voice signal
    E.g. Rectangular pulse function
12
Rectangular pulse function

## Slide 13: SIGNALS: CONTINUOUS-TIME V.S. DISCRETE-TIME
Discrete-time signal
  If the time t can only take discrete values, such as,
  then the signal is a discrete-time signal
  E.g. the monthly average precipitation at Fayetteville, AR (weather.com)
  What is the value of s(t) at ?
    Discrete-time signals are undefined at !!!
    Usually represented as s(k)
13
Monthly average precipitation

## Slide 14
Analog v.s. digital
  Continuous-time signal
    continuous-time, continuous amplitude analog signal
      Example: speech signal
    Continuous-time, discrete amplitude
      Example: traffic light
  Discrete-time signal
    Discrete-time, discrete-amplitude  digital signal
      Example: Telegraph, text, roll a dice
    Discrete-time, continuous-amplitude
      Example: samples of analog signal,
      average monthly temperature
SIGNALS: ANALOG V.S. DIGITAL
1
0
2
3
0
2
1
1
0
2
3
0
2
1
14
Different types of signals

## Slide 15: SIGNALS: EVEN V.S. ODD
Even v.s. odd
  x(t) is an even signal if:
    E.g.
  x(t) is an odd signal if:
    E.g.
  Some signals are neither even, nor odd
    E.g.
  Any signal can be decomposed as the sum of an even signal and odd signal
    proof
even
odd
15

## Slide 16: SIGNALS: EVEN V.S. ODD
Example
  Find the even and odd decomposition of the following signal

## Slide 17
Example
  Find the even and odd decomposition of the following signal
SIGNALS: EVEN V.S. ODD
17
Notes: U = -t  X(u) = 2sin(4u), u > 0  x(-t) = 2sin(-4t), t < 0

## Slide 18
Periodic signal v.s. aperiodic signal
  An analog signal is periodic if
    There is a positive real value T such that
    It is defined for all possible values of t, (why?)
  Fundamental period : the smallest positive integer that satisfies
    E.g.
      So is a period of s(t), but it is not the fundamental period of s(t)
SIGNALS: PERIODIC V.S. APERIODIC
18

## Slide 19: SIGNALS: PERIODIC V.S. APERIODIC
Example
  Find the period of
  Amplitude: A
  Angular frequency:
  Initial phase:
  Period:
  Linear frequency:
19

## Slide 20: SIGNALS: PERIODIC V.S. APERIODIC
Complex exponential signal
  Euler formula:
  Complex exponential signal
  Complex exponential signal is periodic with period
    Proof:
Complex exponential signal has same period as sinusoidal signal!
20

## Slide 21: SIGNALS: PERIODIC V.S. APERIODIC
The sum of two periodic signals is periodic if and only if the ratio of the two periods can be expressed as a rational number.
  The period of the sum signal is
The sum of two periodic signals
  x(t) has a period
  y(t) has a period
  Define z(t) = a x(t) + b y(t)
  Is z(t) periodic?
    In order to have x(t)=x(t+T), T must satisfy
    In order to have y(t)=y(t+T), T must satisfy
    Therefore, if
21

## Slide 22: SIGNALS: PERIODIC V.S. APERIODIC
Example
  Find the period of
  Is periodic? If periodic, what is the period?
  Is periodic? If periodic, what is the period?
  Is periodic? If periodic, what is the period?
Aperiodic signal: any signal that is not periodic.
22
Notes: Tx = 2pi/w = 2 pi/pi/3 = 6
Ty = 2pi/2 = 9
Tz = 2pi/2/9 = 9 pi
Tx/Ty = 6/9 = 2/3, rational, T = lcm(6, 9) = 18
Tx/Tz = 6/(9pi) = 2/(3pi) non-rational

## Slide 23: SINGALS: ENERGY V.S. POWER
Signal energy
  Assume x(t) represents voltage across a resistor with resistance R.
  Current (Ohm’s law): i(t) = x(t)/R
  Instantaneous power:
  Signal power: the power of signal measured at R = 1 Ohm:
  Signal energy at:
  Total energy
  Review: integration over a signal gives the area under the signal.
23
Instantaneous power

## Slide 24: SINGALS: ENERGY V.S. POWER
Energy of signal x(t) over
Average power of signal x(t)
  If then x(t) is called an energy signal.
  If then x(t) is called a power signal.
A signal can be an energy signal, or a power signal, or neither, but not both.
24

## Slide 25: SINGALS: ENERGY V.S. POWER
Example 1:
Example 2:
All periodic signals are power signal with average power:
Example 3:
25
Notes: 1. E = int_0^inf A^2 exp(-2t) dt = A^2 int_0^inf exp(-2t) (-1/2) d(-2t)
= -A^2/2 exp(-2t)_0^inf = -A^2/2 [0-1] = A^2/2
Energy signal
P = E/inf = 0
2. E_T = int_0^T A^2 sin^2(wt+theta) = A^2/2 int_0^T [1 – cos(2wt+2theta)] dt
=A^2/2 int_0^T dt – A^2/2 int_0^T cos(2wt+2theta) dt
= A^2/2 T – A^2/2 int_0^T cos(2wt+2theta) d(2wt+2theta) 1/2w
= A^2/2 T-A^2/2 sin(2wt+2theta)_0^T 1/2w
= A^2/2 T – A^2/(4w) [sin(2wT+2theta) – sin(2theta)]
= A^2/2 T
P = A^2/2  power signal
Sin^2(x) = [1-cos(2x)]/2
wT = 2pi

## Slide 26: OUTLINE
Introduction: what are signals and systems?
Signals
Classifications
Basic Signal Operations
Elementary Signals

## Slide 27: OPERATIONS: SHIFTING
Shifting operation
  : shift the signal x(t) to the right by
  Why right?
27
Shifting to the right by two units

## Slide 28: OPERATIONS: SHIFTING
Example
  Find
28
Notes: (t+3)+1, -1 leq t+3 leq 0
1, 0 < t+3 leq 2
-(t+3)+3, 2 < t+3 leq 3
0, o.w
t+4, -4 leq t leq -3
1, -3 < t leq -1
-t, -1 < t leq 0
0, o.w.

## Slide 29: OPERATIONS: REFLECTION
Reflection operation
  is obtained by reflecting x(t) w.r.t. the y-axis (t = 0)
29
Reflection

## Slide 30: OPERATIONS: REFLECTION
Example:
  Find x(3-t)
The operations are always performed w.r.t. the time variable t directly!
30
Notes: (3-t)+1, -1 leq 3-t leq 0
1. 0 < 3-t leq 2
0 o.w.
-t+4 3 leq t leq 4
1 leq t < 3
0 o.w.
y(t) = x(-t): reflection x(t)
y(t-3) = x(-(t-3))=x(-t+3): move y(t) to the right by 3

## Slide 31: OPERATIONS: TIME-SCALING
Time-scaling operation
  is obtained by scaling the signal x(t) in time.
    , signal shrinks in time domain
    , signal expands in time domain
31
Time scaling

## Slide 32: OPERATIONS: TIME-SCALING
Example:
  scale the signal by a: y(t) = x(at)
  left shift the signal by b/a: z(t) = y(t+b/a) = x(a(t+b/a))=x(at+b)
The operations are always performed w.r.t. the time variable t directly (be careful about –t or at)!
  Find
32
Notes: 3t-6+1 -1 leq 3t-6 leq 0
1 0 < 3t-6 leq 2
-(3t-6)+3 2 < 3t-6 leq 3
0 o.w.
3t-5 5/3 leq t leq 2
1 2 < t leq 8/3
-3t+9 8/3 < t leq 3
0 o.w.

## Slide 33: OUTLINE
Signals
Classifications
Basic Signal Operations
Elementary Signals

## Slide 34: ELEMENTARY SIGNALS: UNIT STEP FUNCTION
Unit step function
Example: rectangular pulse
  Express as a function of u(t)
34
Unit step function
Rectangular pulse

## Slide 35: ELEMENTARY SIGNALS: RAMP FUNCTION
The Ramp function
  The Ramp function is obtained by integrating the unit step function u(t)
35
Unit ramp function
Notes: int_0^t 1 dt = t|_0^t = t

## Slide 36: ELEMENTARY SIGNALS: UNIT IMPULSE FUNCTION
Unit impulse function (Dirac delta function)
  delta function can be viewed as the limit of the rectangular pulse
  Relationship between and u(t)
36
Unit impulse function
Rectangular pulse

## Slide 37: ELEMENTARY SIGNALS: UNIT IMPULSE FUNCTION
Sampling property
Shifting property
  Proof:
37

## Slide 38: ELEMENTARY SIGNALS: UNIT IMPULSE FUNCTION
Scaling property
  Proof:
38
Notes: rect(t/D)
rect(at/D) (area: 1/a)
lim_(D->0) = 1/a delta(t)
rect((at+b)= rect(a(t+b/a)/D)
Or:
p(t)  d to 0  delta(t)
a P(at)  d to 0  a delta( at)

## Slide 39: ELEMENTARY SIGNALS: UNIT IMPULSE FUNCTION
Examples
39
Notes: 3+3^2 = 12
0
tau = 2t – 4
d tau = 2 dt
t = (tau+4)/2
t = -2  tau = -8
t = 3  tau = 2
int_{-8}^2 exp(tau/2+1) delta(tau) 1/2 d tau = 1/2 exp(1)
1/2 delta(t-2)
1/2 int_{-2}^3 exp(t-1) delta(t-2) dt = 1/2 exp(1).

## Slide 40: ELEMENTARY SIGNALS: SAMPLING FUNCTION
Sampling function
  Sampling function can be viewed as scaled version of sinc(x)
40
Sampling function
Sinc function

## Slide 41: ELEMENTARY SIGNALS: COMPLEX EXPONENTIAL
Complex exponential
  Is it periodic?
Example:
  Use Matlab to plot the real part of
41

## Slide 42: SUMMARY
Signals and Classifications
  Mathematical representation
  Continuous-time v.s. discrete-time
  Analog v.s. digital
  Odd v.s. even
  Periodic v.s. aperiodic
  Power v.s. energy
Basic Signal Operations
  Time shifting
  reflection
  Time scaling
Elementary Signals
  Unit step, unit impulse, ramp, sampling function, complex exponential
42